## Slide 1: ECE6130 Project HW4
Group 14

## Slide 2: Part II-A

## Slide 3: 4:1 Column Mux

## Slide 4: Waveform of operation

## Slide 5: Specs
Critical delay:
Delay of nominal VDD:

## Slide 6: Write circuit
Schematic

## Slide 7: Waveform of operation
write data (bit 0)
Write enable
Clock
Bit line output

## Slide 8: Specs
Critical delay: Clk – bitline output delay
Delay of nominal VDD: 178 ps
Power dissipation at nominal Vdd: 118.8uW
Chart: Power vs Delay curve
| 2.8039592461198699E-5 | 5.1558408606807498E-5 | 8.7899188099647599E-5 | 1.18804617683362E-4 | 1.5405932187217701E-4 | 1.9517916938215701E-4 | 2.4337887605745299E-4 | 2.99889842455906E-4 | 3.6577282298047798E-4 | 4.4285065357505497E-4 | 5.32650278928117E-4
Delay | 4.7792e-10 | 2.033e-10 | 2.5168e-10 | 1.7841e-10 | 1.3724e-10 | 1.1324e-10 | 9.802e-11 | 8.7713e-11 | 8.0367e-11 | 7.494e-11 | 7.0813e-11

## Slide 9: Read circuit - Sense Amplifier schematic

## Slide 10: Waveform of operation
Delta = 50mV
Delta = -50mV
Sense amp enable
Sense amp output

## Slide 11: Specs
Critical delay: Sense enable (SAE) to output delay
Delay at nominal VDD: 190 ps
Delta bit (DB) for the sense amplifier: 30mV

## Slide 12: Read circuit

## Slide 13: Specs
Waveform is a trivial extension of the waveform of sense amplifier output. Hence omitted.
Critical delay: Delay between bitline voltages and sense amplifier outputs.
Power at nominal voltage: 30.9uW
Power vs delay curve
(delay at the output register):
Chart: Power vs Delay curve
| 4.1534224739124802E-6 | 1.39272511191142E-5 | 2.2547298390625799E-5 | 3.0907316670236997E-5 | 4.19321037002646E-5 | 5.6499534388581301E-5 | 7.5874823573489895E-5 | 1.01544778614671E-4
Delay Y | 1.481e-12 | 3.9224e-12 | 5.3701e-11 | 3.6941e-11 | 2.8331e-11 | 2.3121e-11 | 1.9606e-11 | 1.7125e-11

## Slide 14: Part II-B: SRAM Cell

## Slide 15: Schematic

## Slide 16: Layout Cell area:

## Slide 17: LVS and DRC Reports

## Slide 18: Specs
  Sizing:
    A sample of many combinations tried.
Sizing (Wp:Waccess:Wpull-down) | Read margin | Read Speed (Cell access time) | Write margin | Comments
1:1.5:2 | 230mV(28%) | 68ps | 260mV(32.6%) | Starting point. Read margin not met. Write margin at the borders. Increase pull-down and check.
1:1.5:2.6 | 243mV(30.3%) | 61ps | 260mV(32.6%) | Specifications met. Improve write margin if possible. Read speed not affected much. Try higher pull-down.
1:1.5:2.8 | 247mV(30.8%) | 60ps | 260mV(32.6%) | Almost same specs, but with increased area. Reduce access.
1:1.3:2.6 | 255mV (31.8%) | 68ps | 240mV (30%) | Approaching sweet-spot. Size pull-up to see if read margin can met with reduced area.
1.2:1.3:2.4, 1.2:1.3:2.6 | 261.1mV (32.6%) | 68.5ps | 260mV(32.6%) | Degrades write margin and area. Reverting to previous sizing. Run parametric analyses to hit the sweet spot.
1:1.4:2.6 | 249.5mV (31.1%) | 64 ps | 280 mV (35%) | Write margin improved by 5%. Minor hit in read margin taken. Final sizing.
2:2.8:5.2 | 248mV (31%) | 32ps | 280mV(35%) | Scaled up to meet layout rules (min. poly as 90nm)

## Slide 19: Sizing plots
Chart: Sizing for write
| 0.33333333333333331 | 0.41666666666666669 | 0.5 | 0.58333333333333337 | 0.66666666666666663 | 0.75
 | 257 | 266 | 272 | 277 | 283 | 285
Chart: Sizing for read
| 1 | 1.3333333333333333 | 1.6666666666666667 | 2 | 2.3333333333333335 | 2.6666666666666665 | 3 | 3.3333333333333335 | 3.6666666666666665 | 4
 | 0.14043 | 0.11453 | 0.096357 | 0.083006 | 0.072828 | 0.064832 | 0.058396 | 0.053108 | 0.048689 | 0.044944
Chart: Sizing for read
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
 | 0.36576 | 0.35337 | 0.34475 | 0.33813 | 0.33275 | 0.32821 | 0.32428

## Slide 20: Access time variations
Chart: Pull down sizing vs cell access time
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 3.78e-11 | 3.28e-11 | 3e-11 | 2.83e-11 | 2.72e-11 | 2.63e-11 | 2.57e-11 | 2.52e-11 | 2.48e-11 | 2.44e-11
Chart: Pull up sizing vs cell access time
| 1 | 1.25 | 1.5 | 1.75 | 2 | 2.25 | 2.5 | 2.75 | 3 | 3.25 | 3.5 | 3.75 | 4
 | 2.9515e-11 | 2.9551e-11 | 2.9582e-11 | 2.9614e-11 | 2.9631e-11 | 2.965e-11 | 2.9669e-11 | 2.9681e-11 | 2.9688e-11 | 2.9692e-11 | 2.9699e-11 | 2.9691e-11 | 2.9689e-11
Chart: Access sizing vs cell access time
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4
 | 7.62e-11 | 5.13e-11 | 4e-11 | 3.37e-11 | 2.96e-11 | 2.69e-11 | 2.49e-11

## Slide 21: Variation with VDD
Chart: VDD vs Read margin
| 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5
 | 0.15824 | 0.19199 | 0.22073 | 0.24361 | 0.26012 | 0.27107 | 0.27793 | 0.28202 | 0.28426 | 0.28524 | 0.28533
Chart: VDD vs Access time
| 0.6 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4 | 1.5
 | 4.62e-11 | 3.76e-11 | 2.96e-11 | 2.43e-11 | 2.08e-11 | 1.83e-11 | 1.64e-11 | 1.5e-11 | 1.39e-11 | 1.3e-11